## Slide 1: Intro to CHIPSEC
Boston Computation Club
Intel CHIPSEC Team: Aaron Frinzell, Dan Scott, Jason Zhou, Nathaniel Mitchell, Sara Batllori
Foundational Cloud DevOps Solutions – Cloud Security and Simics/Cloud Solutions and CHIPSEC

## Slide 2: Legal Notice
No computer system can be absolutely secure.
No license (express or implied, by estoppel or otherwise) to any intellectual property rights is granted by this document.
Intel disclaims all express and implied warranties, including without limitation, the implied warranties of merchantability, fitness for a particular purpose, and non-infringement, as well as any warranty arising from course of performance, course of dealing, or usage in trade.
This document contains information on products, services and/or processes in development. All information provided here is subject to change without notice.
The products and services described may contain defects or errors known as errata which may cause deviations from published specifications. Current characterized errata are available on request.
Intel, the Intel logo are trademarks of Intel Corporation or its subsidiaries in the U.S. and/or other countries.
*Other names and brands may be claimed as the property of others
© Intel Corporation.

## Slide 3: Agenda
  CHIPSEC Overview
  Getting up and running
    Linux
  End to End
Notes: note: OS driver = ring 0
Gain familiarity with Chipsec and its capabilities.
Enable low level platform access through Chipsec module development.
Have Fun and Learn Something.

## Slide 4: Chipsec Overview

## Slide 5: CHIPSEC History
CHIPSEC is a framework for analyzing the security of PC platforms including hardware, system firmware (BIOS/UEFI), and platform components.
Originally developed by Yuriy Bulygin (@c7zero)
First version of CHIPSEC was released in March 2014 at CanSecWest
Currently used by firmware developers, system integrators, system validation and pen testers.
  CHIPSEC GitHub: https://github.com/chipsec/chipsec
  CHIPSEC Documentation: https://chipsec.github.io/

## Slide 6: CHIPSEC Architecture
Chipsec_main.py
Chipsec_util.py
Modules
Tools
Commands
Hardware Abstraction Layer (HAL)
OS Helper
Linux Helper
Linux Driver
Windows* Helper
Windows* Driver
UEFI Helper
UEFI Code
Config
DAL Helper
DAL Code

## Slide 7: CHIPSEC_* Program Flow
Select OS Helpers and Drivers
  Load Driver (optional)
Detect Platform
Load Configuration Files
Load Modules/Utility Command
Run Loaded Modules/Utility Command
Report/Print Results
Clean-up

## Slide 8: Getting up and running
Linux

## Slide 9: Linux – Dependencies
Install or update necessary dependencies for CHIPSEC:
apt-get install build-essential python3-dev python3 gcc linux-headers-$(uname -r) nasm
or
pacman -S python3 python3-setuptools nasm linux-headers
or
dnf install kernel kernel-devel-$(uname -r) python3 python3-devel gcc nasm redhat-rpm-config elfutils-libelf-devel git
Notes: Most of our testing is done on Debian derivatives.
APT = Debian
Pacman = Arch
Dnf = Fedora/RHEL

## Slide 10: Linux – Source, PIP and Build
Clone CHIPSEC source
git clone https://github.com/chipsec/chipsec.git
Install Python Dependencies
pip install -r linux_requirements.txt
Build the Driver and Compression Tools
cd chipsec && python3 setup.py build_ext -i

## Slide 11: Linux – Run
Run chipsec_main.py: sudo python3 chipsec_main.py
Notes: Most of our testing is done on Debian derivatives.

## Slide 12: Return Values
PASSED - Test detected mitigation
FAILED - Test failed to detect mitigation
WARNING - Test results require manual investigation
INFORMATION - Test output is informational only
NOTAPPLICABLE - Test does not apply to current platform (test not run)
ERROR - The test generated an exception

## Slide 13: Other Environments
Windows:
  Windows Installation — CHIPSEC documentation
UEFI Shell:
  Building a Bootable USB drive with UEFI Shell (x64) — CHIPSEC documentation
Notes: Have had issues with v2022, recommend v2019
WDK must match the version of the SDK you have.
For the Driver Downloads, we trust the owner of the repo but we cannot guarantee correctness or safeness of the drivers (because it’s on the internet and we did not put them there ourselves.)

## Slide 14: End to End – Bios Write Protect: Vulnerability > Module > Research

## Slide 15: Setup – Protecting Your Flash
Firmware needs to be secure
  Responsible for system bring-up
  Access to entire software stack
Firmware updates are required
  Feature additions
  Bug patches
Conflict between need of integrity and need for updates
  How is flash memory kept secure?
Notes: System firmware needs to be secure:
At the same time, firmware needs to be updateable:
These two requirements are in conflict with eachother

## Slide 16: Intended Solution
Intel chipset provides flash programming and flash protection features
Flash Programming
  Serial Peripheral Interface (SPI) registers provide control for flash programming operations
Flash Protection
  BIOS Control (BC) and Protected Range (PR) registers are the primary defense against malicious or unintended firmware modification
    3 Fields in BC of interest: SMM_BWP, BiosWE, BiosLE
    PRs can be programmed to mask off specified regions of flash memory as unprogrammable
Notes: Intel chipsets provide features for flash programming and flash protection
Flash programming operations are handled by the SPI
Flash protection is handles by the Bios control and Protected range registers

## Slide 17: Exploiting a Flash Protection Race Condition
Whitepaper by Corey Kallenberg and Rafal Wojtczuk
    https://bromiumlabs.files.wordpress.com/2015/01/speed_racer_whitepaper.pdf
Demonstrates method for subverting flash protections on Intel chipset

## Slide 18: Execution
Works on multicore systems where the BWP field is unset
Attacker programs one core on a tight BiosWE toggle loop
Attacker programs another core to repeatedly attempt a flash programming operation
Flash programming occasionally succeeds before BiosLE unsets BiosWE
Allows attacker to make changes to any portion of BIOS outside Protected Range Masks

## Slide 19: Bypassing Protected Range Masks
UEFI contains non-volatile variables written to flash that need runtime updateability
  Region must be left unprotected by PR masks
Race condition exploit can be used to make arbitrary changes to variable region metadata
  Data within the variable region is treated as trusted by the firmware
  Can be used to gain code execution
  Boot process can be hijacked if instantiated during platform boot
Notes: Depending on the variable targeted, you can modify the flow (Secure boot, boot order, etc) or depending on how FW uses the variables, you could gain code execution in FW.

## Slide 20: Solution Validation
Manufacturers historically failed to set required bits for protection
  Systems left exploitable
CHIPSEC module developed to validate proper write protections
  Bios_WP

## Slide 21: BIOS_WP Module
Checks SMM and SPI based protection mechanisms to ensure BIOS region in flash is write-protected
Inspects BIOS Control register for secure configuration:
  BIOS Lock Enable – Must be set to 1
  BIOS Write Enable – Must be set to 0
  SMM BIOS Write Protection – Must be set to 1
Checks SPI Protected Ranges
  BIOS region must be covered by PRs

## Slide 22: Demo

## Slide 23: Thank you
Looking forward to your future research & CHIPSEC contributions!
Any additional feedback is welcome at chipsec@intel.com
CHIPSEC Discord Server https://discord.gg/NvxdPe8RKt

## Slide 24: Questions? Try it yourself!
Notes: We still have x amount of time. I believe you all have an ADL NUC, if you want to try installing and running chipsec in this meeting, we are here to help if you run into any issues.

## Slide 26: References
Chipsec
  https://github.com/chipsec/chipsec
Chipsec Documentation
  https://chipsec.github.io

## Slide 27: Troubleshooting Windows:
Is driver signing disabled?
Driver build error: Recommend using VS2019. SDK and WDK should match the OS you are running (11 for Win 11, 10 for Win 10)
Windows: Python not in path / won’t run from command-line’ When installing Python support, make sure the installer is run in Administrator Mode` and ensure to add to environment variable is checked. It is NOT a CHIPSEC error. Easiest way to fix is to rerun the Windows Python installer and select Add Python to environment variables. Exact text may change from version to version
No module named pywintypes This is error is indicating that Python cannot find the pywin32 module. Basically, the Python Windows Extension dependency, pywin32, was not installed. To fix, verify that the appropriate PyWin32 module is installed on the system. Location of these modules are covered in the Windows Prerequisite section earlier in this document. Example error: 22 - Using CHIPSEC ImportError: No module named pywintypes

## Slide 28: Troubleshooting Linux
Did you use sudo?
/bin/sh: 1: nasm: not found Makefile:22: recipe for target 'chipsec64' failed make: ***[chipsec64] Error 127 Make sure you install all prerequisites.
Clock Skew Detected This error seems to occur when building the driver and the build system Date / Time are not set properly. Setting the system date and time should correct this issue. make: warning: Clock skew detected. Your build may be incomplete.

## Slide 29: Firmware/Chipsec/Security Acronyms
(U)EFI | (Unified) Extendible Firmware Interface |  | GUID | Globally Unique Identifier |  | PPI | PEIM-to-PEIM Interface
EDK2 | EFI Development Kit II |  | HAL | Hardware Abstraction Layer |  | Ptr | Pointer
ABI | Application Binary Interface |  | HOB | Hand-off Block |  | ROM | Read Only Memory
ACPI | Advanced Configuration and Power Interface |  | I/O | Input Output |  | RCS | Remote Control System
AKA | Also Known As |  | IPI | Inter Processor Interrupt |  | RSM | Resume instruction
AL | After Life |  | MMI | Management Mode Interrupts |  | RT | Run Time
API | Application Programming Interface |  | MS | Microsoft* |  | (S)MM | (System) Management Mode
APIC | Advanced Programmable Interrupt Controller |  | NTFS | New Technology File System |  | SAL | Software Architectural Layer
BAR | Base Address Register |  | NVRAM | Non-Volatile Random Access Memory |  | SEC | SECurity phase
BDS | Boot Device Select |  | ODM | Original Design Manufacturing |  | SMBIOS | System Management BIOS
BIOS | Basic Input Output System |  | OEM | Original Equipment Manufacturing |  | SMI | System Management Interrupt
C&C | Command and Control |  | OS | Operating System |  | SMRAM | System Management Random Access Memory
CPU | Central Processing Unit |  | OVMF* | Open Virtual Machine Firmware |  | SMST | System Management System Table
DXE | Driver Execution Environment |  | PC | Personal Computer |  | SPI | Serial Peripheral Interface
FD(F) | Flash Descriptor File |  | PCD(S) | Platform Configuration Database(s) |  | SW | Software
FTW | Fault Tolerant Write |  | PCH | Platform Controller Hub |  | TPM | Trusted Platform Module
FV | Firmware Volume |  | PCI | Peripheral Component Interconnect |  | TSEG | Top SEGment
GAS | Generic Access Structure |  | PE | Portable Executable |  | TSL | Transient System Load
gBS | Global Boot Services |  | PEI(M) | Pre-EFI Initialization (Module) |  | UINT | Unsigned integer
Third party components are marked with an (*) throughout the presentation